Introduction to the Techniques Used in AP Lab #6 and PCR

© Rob Hamilton

Purpose:  The laboratory introduces micropipeting and sterile techniques that will be used in future experiments.  Mastery of these techniques is important for good results in the experiments that follow.  Most of the laboratories are based on protocols involving very small volumes of DNA and reagents.  These require you to use an adjustable micropipet that measures as little as one microliter (μl)--a millionth of a liter!

A)  Fun with Metric Conversion

It is important to become familiar with metric units of measurement and their conversions.  We will concentrate on liquid measurements (based on the liter).  These volumes are so small that it will be difficult for you to see them on the side of the Eppendorf tube.   The two most prevalent units of liquid measurement in molecular biology are the milliliter (ml) and the microliter (μl).

Examine the following equivalencies:  1 ml = 1/1,000 liter and 1 μl = 1/1,000,000 liter

With the above information in mind, complete the following conversions.  We will check your answers as a class before we continue.

1 μl = ___________________ ml			10 μl = ___________________ ml

100 μl = ___________________ ml			___________________μl = 1 ml

B)  Proper Use of Ultra Digital Micropipets  (Come to a lab station for a demonstration)

The micropipets you are using cost approximately $300.00 each and can easily be destroyed by an inattentive student.

Remember these important DON’TS when using either the 2000 or 2001 series pipets

1.  Never move the pipet out of its intended range because the screw which controls the volume will be stripped and the pipet will be irreparably damaged.  Micropipets operate between 100 μl and 1000 μl.

Ultramicropipets operate between 1 μl and 10 μl.  MAKE SURE YOU KNOW WHICH ONE YOU ARE HOLDING IN YOUR HAND!

2.  Never attempt to use a pipet without a tip as the fluid will be sucked into the piston, destroying the pipet.

3.  Never lay down a pipet with a filled tip as fluid will run back into the piston.  Always hold the pipet vertically with the tip down!

4.  Never let the plunger snap back after withdrawing or ejecting fluid.  The bore of the pipet tip is very narrow and the fluids might “fountain” up into the piston.

2000 series (the longer pipet) only:

5.  Never attempt to change the volume without unlocking the control knob.

6.  Never leave the metal piston on the 2000 series ultramicrodigital pipet exposed.  Always cover it with a tip.

C.  Ultra Digital Micropipeting Proceedure:

1.  Push the pipet firmly into the proper sized tip. There is a gap between the pipet barrel and the tip.  Don’t force the gap to go away because it will crack the tip and the pipeter will suck air through the crack instead of liquid up the tip.  The tip is sterile, you are not. Do not touch the tip.  Always keep the lid on the tip box covered because we don’t want to invite airborne contaminants.

2.  Set the pipet to the desired volume.  With the 2000 series pipets you will have to pull up on the control knob until you hear a click.  Rotate the button until you encounter the desired volume in the window.  You do not need to rotate the knob slowly but you must watch the window to ensure that you do not take the pipetter out of its range.   With the 2000 series pipets you will have to now depress the control knob to lock the volume into place.

3.  Have your partner hand you the reagent tube from which you will be drawing liquid.  Partners should repeat the amount which should be pipeted.  Hold the Eppendorf tube at eye level.  Now depress the plunger to the first stop.

4.  Dip the tip into the solution to be pipeted and draw fluid into the tip by gradually releasing the plunger.  You must watch as you pipet.

5.  Slide the tip out along the inside wall of the Eppendorf tube to dislodge any excess fluid adhering to the outside of the tip.  Many reagents are gooey so it is easy to over pipet.

6.  Touch the pipet to the inside wall of the Eppendorf tube into which you want to empty the sample.  This action creates a capillary effect which helps draw the fluid out of the tip.

7.  To expel the sample, slowly depress the plunger to the first stop.  Now press on to the second stop to blow out the last bit of fluid while you stroke the tip up the side of the tube.  Failure to do this can cause the sample to be sucked back into your tip and you might never know it.

8.    Visually confirm that your reagent is on the side wall of the tube.

9.  Eject the tip into the waste beaker (labeled “Spent Tips”).  2000 series ejects by moving the plunger to the 3rd stop.  2001 series uses a separate tip eject on the thumb side below the plunger.

D.  Initial Ultra Digital Micropipeting Practice:

Now go to your station and engage yourselves in some unstructured practice with the ultrmicropitets by transferring blue solution #2 to the Eppendorf tube labeled “P” for practice.  Watch your partner complete the 9 steps above.  Make sure you practice with a volume between 10-7 μl, one between 6-2 μl and a 1 μl sample.  Keep practicing until pipetting is second nature and then return to your desks.

E.  Proper Use of a Microcentrifuge

Our lab has 3 brands of microcentifuge in use.  The International has 4 slot head, an on/off switch and a manual brake.  The Clay-Adams has a 6 slot head, a speed control knob and no brake.  The Eppendorf 5451C has an 18 slot head, a momentary button (for short spins) and a magnetic brake.  Because of the high speeds achieved by the motor (14,000 rpm with a centrifugal force of 16,000 gravities), it is essential that the rotor head is balance.  Come to the front table for a demonstration.

F.  Final Ultra Digital Micropipeting Excersize:

1.  Use the three Eppendorf tubes labeled A, B, and C.

2.  Use the matrix below as a checklist.  Each time you add a reagent to a tube, make a checkmark on the blank after the reagent volume.

3.  Add solution #1 to all the required tubes.  Change your tip and then add solution #2 to the required tubes.  Change your tip and add solution #3 to each required tube.  Change your tip and add solution #4 to all the required tubes.  Each partner should do two solutions.  (This allows you to blame your partner for any inaccurate pipeting.)

REAGENTS

Tube		Solution #1		Solution #2		Solution #3		Solution #4

A			4 μl  _____		5 μl  _____		1 μl  _____		      None

B			4 μl  _____		5 μl  _____		     None		1 μl  _____

C			4 μl  _____		4 μl  _____		1 μl  _____		1 μl  _____

4.  Tightly close all the tops of the Eppendorf tubes and place them in a balanced configuration in your microcentrifuge rotor head.  Spin the liquid to the bottom of the tube by turning on the microcentrifuge for the time listed below:

a)  The International Microcentrifuge will require a 1 minute spin

b)  The Clay-Adams will require a 30 second spin

c)   The Eppendorf 5415C will require a 10 second pulse.

Accuracy Check:

1.  You added a total of 10 μl of reactants to each Eppendorf tube.  Now we will check your accuracy.  Set your pipet at 10 μl and carefully withdraw the solution from tube A.  Seat your pipet tip on the bottom of the Eppendorf tube and slowing releasing the plunger.

a)  Are you able to fill the tip with no solution left in the tube?  (circle one)     Yes	 No

b)  What does this tell you about your technique?  (circle one)    perfect      overpipeting        under pipeting

c)  Is there a small air space left in the tip after extracting all the fluid in the tube?  (circle one)     Yes	    No

d)  What does this tell you about your technique?  (circle one)    perfect       overpipeting        under pipeting

e)  Is the tip filled along with fluid remaining in the Eppendorf tube?  (circle one)     Yes	    No

f)  What does this tell you about your technique?  (circle one)   perfect         overpipeting       under pipeting

e)  In the winter, the pipets will typically under pipet slightly.  Why would this be so?  __________________

_____________________________________________________________________________________

2.  Discard the fluid in the spent tips beaker and repeat the check for tubes B and C.

G.  Digital Micropipeting Excersize:

1.  Use the Eppendorf tubes labeled D, and E.

2.  Use the matrix below as a checklist.  Each time you add a reagent to a tube, make a check mark on the blank after the reagent volume.

3.  Add solution #1 to all the required tubes.  Change your tip and then add solution #2 to the required tubes.  Change your tip and add solution #3 to each required tube.  Finally, change your tip and add solution #4 to all the required tubes.

Reagents

Tube		Solution #1		Solution #2		Solution #3	 	Solution #4

D			100μl  _____		200μl  _____		550μl  _____		150μl  _____

E			150μl  _____		250μl  _____		350μl  _____		250μl  _____

4.  Close all the tops of the Eppendorf tubes.  Large volumes naturally sink to the bottom of the Eppendorf tubes, so there is no reason to spin down the fluid.

Accuracy Check:

1.  You added a total of 1000 μl of reactants to each Eppendorf tube.  Now we will check your accuracy.  Set your pipet at 1000 μl and carefully withdraw the solution from tube D.  Slowly move you pipet tip to the bottom of the Eppendorf tube as you gradually release the plunger.

a)  Are you able to fill the tip with no solution left in the tube?  (circle one)     Yes	 No

b)  What does this tell you about your technique?  (circle one)  perfect         overpipeting        under pipeting

c)  Is there a small air space left in the tip after extracting all the fluid in the tube?  (circle one)     Yes	    No

d)  What does this tell you about your technique?  (circle one)  perfect         overpipeting        under pipeting

e)  Is the tip filled along with fluid remaining in the Eppendorf tube?  (circle one)     Yes	    No

f)	What does this tell you about your technique?  (circle one)  perfect         overpipeting      under pipeting

2.  Discard the fluid in the spent tips beaker and repeat the check for tube E.

H.  Maintaining Sterile Technique

In the transformation lab we will be working with E. coli mm294.  This is a genetically crippled strain of bacteria

that cannot grow outside of ideal conditions.  My main concern is not E. coli getting on you....I am worried about you introducing bacteria into our growth medium (Luria-Bertani broth and agar).  Contamination will not only ruin your results, but more importantly, it has the potential to be a health risk.  This is not something to be taken lightly......YOUR HEAD MUST BE ON TASK AT ALL TIMES.  I will briefly discuss the instruments involved in the transformation and the protocols that are required to keep them sterile.  Come to the front table for a demonstration.

1.  Inoculating Loops:  We use individually wrapped loops that are sterile.  Unwrap the end away from the loop and do not touch the loop to any surface and it will remain sterile.

2.  Falcon Tubes:  The Falcon tubes are initially sterile, but the potential for contamination increases when they are opened.  When opening a Falcon Tube:

a)  Firmly grasp the lid and pull it off the tube.

b)  Every time you open a Falcon tube, flame both the lid and the tube by moving them quickly through the Bunsen burner flame.  NOTE:  The flaming doesn’t kill microorganisms; it simply creates convection current out of the tube reducing the chances of an airborne contaminant entering.

c)  Never set the lid on the lab table and always hold it with the opening down.

d)  Hold the Falcon tube near the bottom and as close to parallel with the ground as you can without spilling its contents.  This reduces the chance of bacteria entering from the air.

e)  Flame the Falcon tube and cap again after you have added anything to the tube and then recap the tube.

3.  Petri Plates:  Open Petri plate only as much as necessary to gain access to its contents.  Always keep the lid above the plate and never place it on the lab table.

4.  Cell Spreaders:  Cell spreaders are used to evenly spread bacterial solutions onto a Petri plate.

a)  To prevent cross contamination of bacterial cultures, cell spreaders are place in a 95% ethanol solution for a minimum of 15 seconds.

b)  Excess ethanol is then removed by flaming.

c)  Do not allow the flaming liquid ethanol to run back down on your hand or clothes.

d)  Use extreme care to avoid igniting the ethanol beaker

e)  Cool the spreader on agar away from the bacteria before spreading.

5.  Pipet Tips:  The tips in the box are sterile and will stay that way unless they touch something.  Always keep the lid on the tip box and never put the lid on the lab table.

If a bacterial solution is spilled, tell Mr. H immediately and I will bring a solution used for decontamination